## Slide 1
1. Tan Tai Boon, A. J. Schultz, and D. A. Kofke, 'Efficient Calculation of - and -Nitrogen Free Energies and Coexistence Conditions Via Overlap Sampling with Targeted Perturbation', Journal of Chemical Physics, 135 (2011), 044125 (13 pp.).
2. T. B. Tan, A. J. Schultz, and D. A. Kofke, 'Efficient Calculation of Temperature Dependence of Solid-Phase Free Energies by Overlap Sampling Coupled with Harmonically Targeted Perturbation', Journal of Chemical Physics, 133 (2010).
1.Solve the blockage in the oil pipelines.
The formation of clathrate hydrate becomes the main reason of blockage in the pipelines which could result in the suspension of gas and oil production. It is also one of reason of ecological disasters like tragedy in the Mexico Gulf.
2. Structure
Gas hydrates usually form three crystallographic cubic structures: structure I and structure II and Structure H. Each type are formed of two or three small cages:
A Comprehensive Molecular-Based Study of the Stability of clathrate Hydrates
Weisong Lin , Andrew J. Schultz, David A. Kofke
Department of Chemical and Biological Engineering, University at Buffalo, The State University of New York, Buffalo, NY 14260
Introduction
clathrate hydrate. The Bones are H20 and the green Spheres are guest molecules
http://ps.uci.eduscholarkcjandaresearchgas-hydrate-structure
The three common clathrate hydrate structures, including the constituent cavities. Nomenclature: 51268indicates 12 pentagonal and 8 hexagonal sides in a cavity; numbers along lines indicate the number of cavities in each unit crystal structure. The rightmost numbers indicate the water molecules per crystal structure
http://www.globalspec.com/reference/55602/203279/2-what-are-natural-gas-clathrate-hydrates
1. Definition
Clathrate hydrates are crystalline structures that consist of water molecules forming cages via a hydrogen-bonding network enclosing small guest molecules. Such structures normally form at a condition of high pressure and low temperature.
Motivation
Pipeline blockage caused by clathrate Hydrate
http://www.radhanathswamionline.comeventshow-to-fix-the-hole-in-the-gulf-of-mexico
disaster of oil in the Gulf of Mexico
http://www.radhanathswamionline.comeventshow-to-fix-the-hole-in-the-gulf-of-mexico
2. Recovery of huge potential energy
The global resource of methane in gas hydrate deposits in commonly cited as 20,000 trillion m3 making gas hydrates itself contain more energy than any other forms of energies we exploit today. Exploiting the resource while capturing CO2 would not only solve the energy crisis but also reduces the greenhouse gases.
Flaming hydrate
www.chem.ntnu.nononequilibrium-thermodynamicsindex522b.html
clathrate hydrate with vacant cages.
structure Energy science of clathrate hydrates Simulation-based advances Amadeu K. Sum , David T. Wu , and Kenji Yasuoka
3. Clathrate hydrate also has other applications in refrigeration, desalination and transportation.
Solid-fluid secondary refrigerants have higher energy efficiency in refrigeration. Advances are reported in several aspects of clathrate hydrate desalination fundamentals necessary to develop an economical means to produce municipal quantities of potable water from seawater. Using clathrate transport gas like H2 would be safer and more efficient by reducing pressure and increasing temperature.
Method
1. Use harmonic analysis to find the free energy of clathrate hydrate with all cages vacant when temperature→ 0.
World-gas-hydrates-locations
www.eaglespeak.us201303mining-methane-hydrate-and-what-it-means.html
2. Introduce harmonically targeted temperature perturbation (HTTP) method to evaluate the free energy with increasing temperature.
3. Conduct additional molecular simulations to gauge the dependence on composition and/or pressure by integration along μS
4. With the knowledge of free energy we can identify the stable crystalline form and locate the conditions where phase transitions occur.
Preliminary Result
Generation of the clathrate structure type I
Methane hydrate presure-temperature phase diagram
http://commons.wikimedia.org/wiki/File:Methane_Hydrate_phase_diagram.jpg
Method Advantages
1. No system size dependence
Dependence of free-energy contributions on the size of the simulated
Tan, T. B.; Schultz, A. J.; Kofke, D. A., Efficient calculation of α- and β-nitrogen free energies and coexistence conditions via overlap sampling with targeted perturbation. J. Chem. Phys. 2011, 135
(4), 044125.
2. Much more precise than FEP theory
When temperature is 0, we could do the harmonic analysis (configuration space is circle). But when temperature get higher, system become enharmonic(not circle) and configuration space increases rapidly with temperature. If we do the scaling, difference would be smaller.
Temperature perturbation method. Measuring ΔβA with perturbation fails
http://rheneas/~andrew/http/HTTP.xhtml
HTTP method. Scale out the change in size we expect
http://rheneas/~andrew/http/HTTP.xhtml
References
Acknowledgements
Notes: <number>